2001-07-12

Network Working Group

TASK STATUS REPORT

Status codes

DI - Dispute to Coord Committee

U - Underway

CR - Complete with Report

CD - Complete with Commission Decision

| TIF File Name | Task Definition | Status | Notes | Estimated Date of Completion |
| --- | --- | --- | --- | --- |
| TITF006 | Calling Name Interworking Intermediate 10 D GTT required if there are more than one Database | Parked | Required to support a 2nd Calling Name Database. Work will only commence when a 2nd database is required. |  |
| NPTF001 | Transiting - phase 2 Investigate transiting architecture where CLECs deploy access tandems | Parked | It was agreed not to proceed with this activity pending outcome of Network of Networks activities. |  |
| NPTF002 | LECs to disclose POI/SPOI locations | U | POI/SPOI locations are posted in the CRTC CISC NTWG web page | ongoing |
| NPTF005 | Forecast Data | U | Joint work activity with BPWG to revise unbundled loop forecast information. The current forecast information is specified in consensus report NTRE003. | 4Q01 |
| NTTF004 | Voice over IP (VoIP) | U | This TIF is to address the impact of IP technology on the current interface arrangements and interface specifications. Over 20 contributions were submitted for this TIF. There is consensus on some technical questions. However, some of the interconnection issues cannot be resolved until more fundamental questions of regulatory framework on emerging technologies are resolved. The NTWG has started to prepare a VoIP status report (NTCO129b) for this TIF. | 4Q01 (report) |
| NTTF005 | Wireless CLEC - Impact of Roaming | CR CR U | Consensus report NTRE008 accepted by Steering Committee. Report NTRE009 accepted by Steering Committee. Work continues to investigate standard solution to identify locations of roaming mobile terminals | Feb/01 Jun/01 2Q02 |
| NTTF006 | Centrex Interworking | U | Task objective is to determine a Centrex Minimum Feature Set (CMFS) that would support interworking between Centrex users, belonging to the same Centrex Multi-location Business Group in different LEC switches, and to develop an associated network-to-network interface specification. Testing has revealed interworking problems between vendor software (NTCO127). Some issues have been resolved while others are being pursued with switch vendors. Testing on hold pending problem resolution. | 2Q02 |
| NTTF007 | Toll Free Interface | CR | Consensus toll-free interface specification (NTRE010.doc) accepted by Steering Committee. Contribution (NTCO133) submitted on toll-free call flow. | Jun/01 |
| NTTF008 | Spectrum Management (SM) | U | TIF approved by Steering Committee on Jun 01/01. Contributions submitted on Hazardous Voltages (NTCO130) on loops and SM deployment guidelines (NTCO131). Letters sent to TAPAC and other WGs to initiate SM work in these groups. | 1Q02 |